| Aircraft Questionnaire |  |
| --- | --- |

Pilot Name: _________KEY________________  A/C: N___________ Type/Model Acft: _________

Check Pilot: _____________________________  Score:____________ Date: ___________________

Complete this open book questionnaire using the Flight Manual/Pilot’s Operating Handbook.  If a question or part of a question is not applicable, write in NA.  The check pilot will review and grade the questionnaire.  Minimum passing score is 80%.  The completed questionnaire will be filed in the pilot’s flight records.

- Approved fuel grades and colors are:        100LL (Blue), 100 (Green)       P.1-3

- Location / capacity of each fuel tank is:  Wing Tanks w/ 21.5 gallons each (48 gal. total)  P.1-4

- Total usable fuel under all flight conditions is __40  P.1-4_gallons.

- Endurance at 75% power, 7,400 feet MSL, with a 45 min. reserves ___4:03   P.5-19_hours.

- What make and grade oil is used?  SAE 50, SAE 40, SAE 30, SAE 20    P.1-4    (we use______)

- Oil capacity is _7_ P.2-5_ quarts.  Minimum oil quantity for takeoff is _4__P.4-5_quarts.

- Minimum oil pressure is __25__ psi.  Maximum oil pressure is __100_ _psi.   P.2-5

- Maximum oil temperature is _245_ oF or _118__ oC.  P.2-5

- Magnetos are checked at _1700__ RPM.  RPM drop should not exceed ___125___RPM on either magneto or __50__ RPM differential between magnetos.   P.4-13

- Maximum RPM and MP for takeoff are _2700__ and ___N/A_ in/Hg.    P.2-5 (2280-2400 static)

- Maximum gross takeoff weight is __2300__ lbs.  Empty weight is _1393__ lbs. P.1-5 ours _____

- Baggage compartment locations/weights are: 1 = station 82-108, 120# -- 2 = 108-142, 50#  P.1-5

- Give the IAS at maximum gross weight for:

  - Va (maneuvering speed)                           97 KIAS      P.2-5

  - Vso (stall, landing config, power off)       41 KIAS         “

  - Vs1 (stall, cruise config, power off)          47 KIAS        “

  - Vy (best rate of climb, sea level)              73 KIAS      P.4-3

  - Vx (best angel of climb, sea level)           59 KIAS      P.4-3

  - Vfe (max speed with flaps extended)       85 KIAS       P.2-5

  - Vno (maxium speed for normal ops)       128 KIAS         “

  - Vne (never exceed speed, redline)          160 KIAS         “

  - Best glide speed                                       65 KIAS         “

- Give the immediate action/memory items for:

Engine failure immediately after takeoff: Airspeed 65 KIAS (flaps up or 60 KIAS flaps down)Mixture – Idle cut-off, Fuel selector –off, Ignition  – off, flaps – A/R, master – off P3-4

Fire during cranking and engine fails to start: Cranking –continure, throttle – full open, Mixture – Idle cut-off         P.3-5

Engine fire in flight: Mixture-Idle cut-off, Fuel selector – Off, Master – off, Cabin heat & Air-Off, Airspeed – 100 KIAS, Forced Landing – Execute_________ P.3-6

Electrical fire in flight: Master – off, Avionics – off, all other switches – off, vents/cabin air/ heat – closed, Fire extinguisher – activate_____________ P.3-6

- Normal takeoff flap setting is __0o____, short field takeoff setting is __0o_____, and soft field takeoff flap setting is __10o_____.      P.4-14

- Maximum demonstrated takeoff/landing crosswind component is __15___ knots.   P.4-3

- Given:  PA=4,000 feet; Temp=86oF; Runway 27; Wind 320o at 14 knots; runway is paved, level, and dry; aircraft is at maximum landing weight.

Find: Total takeoff distance to clear a 50 foot obstacle __2101.5 ft.___.     P.5-12

- Given:  PA=6,000 feet; Temp=86oF; wind calm; runway is paved, level, and dry; aircraft is at maximum landing weight.

Find: Total takeoff distance to clear a 50 foot obstacle ___2895____.    P.5-12

- Landing runway 22; wind 190o at 22 gusting to 30 knots.  Will the maximum demonstrated crosswind component for this aircraft be exceeded?    NO – X-Wind is right at 15 kts.(26 kts HW)