| C-172 N | N – 737RR |  | July 9 2000 Wt & Bal Empty Weight 1481 ibs ARM 38.44 inches Moment 56929.2 |
| --- | --- | --- | --- |
| Date: |  |  |  |
| PIC: |  |  | Weight (lbs) | Arm (in.) | Moment (in./lbs) |

| Aircraft Basic Empty Weight |  |  |  |
| --- | --- | --- | --- |
| Usable Fuel (40 Gal x6 lbs/gal) | + | x 48.0 | + |
| Pilot and Copilot | + | x 37.0 | + |
| Rear Passengers | + | x 73.0 | + |
| *Baggage Area 1 (120 lbs Max) | + | x 95.0 | + |
| *Baggage Area 2 (50 lbs Max) | + | x 123.0 | + |
| Start, Taxi, Runup Fuel | -7.0 | x 48.0 | - 336 |
| Takeoff Weight / CG / Moment |  |  |  |
| Planned Flight Fuel Usage (9 gals per hour) | - | x 48.0 | - |
| Landing Weight / CG / Moment |  |  |  |

NOTE:	*The maximum allowable combined weight capacity for baggage areas 1 and 2 is 120 lbs.

CG (in) = Sum of Moments / Sum of Weights

Write Takeoff and Landing CG in Arm Column Above, Mark on Diagram Below

| C-172N | N - | Temp: | PA: |
| --- | --- | --- | --- |
| TO Dist: | Land Dist: |

TAKEOFF DISTANCE

maximum weight 2400 lbs

short field

CONDITIONS:

Flaps Up

Full Throttle Prior to Brake Release

Paved. Level, Dry Runway

Zero Wind

NOTES:

- Short field technique as specified in Section 4.

- Prior to takeoff fields above 3000 feet elevation, the mixture should be leaned to give maximum RPM in a full throttle, static runup.

- Decrease distance 10% for each 9 knots headwind.  For operation with tailwinds up to 10 knots, increase distances by 10% for each 2 knots.

- For operation on a dry, grass runway, increase distance by 15% of the “ground roll” figure.

| weight lbs | takeoff speed kias | press alt ft | 00C | 100C | 200C | 300C | 400C |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | lift off | at 50 ft |  | grnd roll | total to clear 50 ft obs | grnd roll | total to clear 50 ft obs | grnd roll | total to clear 50 ft obs | grnd roll | total to clear 50 ft obs | grnd roll | total to clear 50 ft obs |
| 2400 | 51 | 56 | S.L. 1000 2000 3000 4000 5000 6000 7000 8000 | 795 875 960 1055 1165 1285 1425 1580 1755 | 1460 1605 1770 1960 2185 2445 2755 3140 3615 | 860 940 1035 1140 1260 1390 1540 1710 1905 | 1570 1725 1910 2120 2365 2660 3015 3450 4015 | 925 1015 1115 1230 1355 1500 1665 1850 2060 | 1685 1860 2060 2295 2570 2895 3300 3805 4480 | 995 1090 1200 1325 1465 1620 1800 2000 ----- | 1810 2000 2220 2480 2790 3160 3620 4220 ----- | 1065 1170 1290 1425 1575 1745 1940 ----- ----- | 1945 2155 2395 2685 3030 3455 3990 ----- ----- |

LANDING DISTANCE

short field

CONDITIONS:

Flaps 300		Power Off		Maximum Breaking		Paved. Level, Dry Runway	Zero Wind

NOTES:

- Short field technique as specified in Section 4.

- Decrease distance 10% for each 9 knots headwind.  For operation with tailwinds up to 10 knots, increase distances by 10% for each 2 knots.

- For operation on a dry, grass runway, increase distance by 45% of the “ground roll” figure.

- If a landing with flaps up is necessary, increase the approach speed by 7 KIAS and allow for 35% longer distance.

| weight lbs | speed at 50 ft kias | press alt ft | 00C | 100C | 200C | 300C | 400C |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | grnd roll | total to clear 50 ft obs | grnd roll | total to clear 50 ft obs | grnd roll | total to clear 50 ft obs | grnd roll | total to clear 50 ft obs | grnd roll | total to clear 50 ft obs |
| 2400 | 61 | S.L. 1000 2000 3000 4000 5000 6000 7000 8000 | 510 530 550 570 595 615 640 665 690 | 1235 1265 1295 1330 1365 1400 1435 1475 1515 | 530 550 570 590 615 640 660 690 715 | 1265 1295 1330 1360 1400 1435 1470 1515 1555 | 550 570 590 615 635 660 685 710 740 | 1295 1325 1360 1395 1430 1470 1510 1550 1595 | 570 590 610 635 660 685 710 735 765 | 1325 1360 1390 1430 1470 1510 1550 1590 1635 | 585 610 630 655 680 705 730 760 790 | 1350 1390 1425 1460 1500 1540 1580 1630 1675 |